#### DEB Packages (Debian OS)
AutomataCI supports DEB packages by default using its own packager based on Debian specification. This approach was required mainly because the toolkit provided by Debian OS is too massive and some are deviated from the specifications (e.g. excessive checking).

Although AutomataCI uses its own compiler, the output shall always be compliant with upstream. you’re still required to learn through the specifications (at least binary package) shown above before proceeding to construct the job recipe. The supporting documentations AutomataCI based on are as follows:
1. https://www.debian.org/doc/debian-policy/index.html
2. https://manpages.debian.org/unstable/dpkg-dev/deb.5.en.html
3. https://refspecs.linuxfoundation.org/FHS_3.0/fhs/index.html

AutomataCI prioritizes binary package build since the source codes are usually distributed using git control ecosystem. This removes any duplication related to the project and focus on customer delivery instead.

Windows OS is not supported mainly due to the lack of UNIX permission manipulation (e.g. chmod or chown commands).

Starting from version 2.0.0, AutomataCI package DEB type in parallel execution.

##### Supported Platforms
The current AutomataCI supported host platforms are shown in Table 1.
Table 1: DEB packaging support status
Platform	Supported	Tested	Automated Test
linux-amd64 (Debian)	Yes	Yes	Yes
linux-amd64 (Red Hat - Fedora)	Yes	No	Yes
darwin-amd64 (Intel-based MacOS)	Yes	Yes	Yes
windows-amd64	No	No	N/A

NOTE:
“N/A” – means “Not Available”.
##### Content Assembling Function
The content assembling function is shown in Table 2.
Table 2: the content assembly function symbol for DEB packager
# POSIX Shell / PACKAGE_Assemble_DEB_Content() { / _target="$1" / _directory="$2" / _target_name="$3" / _target_os="$4" / _target_arch="$5" / … / }
# PowerShell / PACKAGE-Assemble-DEB-Content { / param( / [string]$_target, / [string]$_directory, / [string]$_target_name, / [string]$_target_os, / [string]$_target_arch / ) / … / }

The $_directory variable should point to the workspace directory containing 2 important directories:
1. control/ – housing the control components of the .deb package; AND
2. data/ – housing the data components of the .deb package.

The objectives are:
1. to assemble the “to be installed” file structure in the data/ directory complying to Filesystem Hierarchy Standard; AND
2. to assemble any maintainer scripts (if needed) in the control/ directory.
For example:
1. the provided $_target variable that is pointing to the currently detected binary executable. It is usually being copied to ${directory}/data/usr/local/bin/ directory.
  1. This means that the package shall the target program into /usr/local/bin/ when the package is installed by the customer.
AutomataCI provides sufficient utilities to create all the required files. It’s entirely your duty to assemble all the files in their respective location and only create the control/control file as the last step due to its requirement of calculating data/ directory disk space consumption.
The following return numbers to tell AutomataCI to perform the necessary actions:
1. 10 – Tell AutomataCI to skip the packaging process.
2. 0 – All good and proceed.
3. non-0 – Error is found.
##### Required Files
This packager has the following required files:
1. data/usr/share/docs/${PROJECT_SKU}/changelog.gz
   OR
   data/usr/local/share/docs/${PROJECT_SKU}/changelog.gz
2. data/usr/share/docs/${PROJECT_SKU}/copyright.gz
   OR
   data/usr/local/share/docs/${PROJECT_SKU}/copyright.gz
3. data/usr/share/man/man1/${PROJECT_SKU}.1.gz
   OR
   data/usr/local/share/man/man1/${PROJECT_SKU}.1.gz
4. control/md5sum
5. control/control
These files follow strict format and content as specified in the Debian manual (especially control/control file).
##### Maintainers’ Scripts
As frown by the Debian specification when used for installing files and directories, maintainers’ scripts are only used when required. Manual efforts can cause unwanted and unclean executions at the end-user sides.

These optional scripts are usually used for emergency and adaptive patching, services (e.g. systemd, cron, nginx, etc) signaling and control before or after an install or uninstall process.

Supported Maintainers’ scripts are:
1. control/preinst – commands before install
2. control/postinst – commands after uninstall
3. control/prerm – commands before uninstall
4. control/postrm – commands after uninstall

When in doubt, use post[ACTION] instead.
##### AutomataCI’s Copyright.gz Generative Function
AutomataCI constructs the copyright.gz file by generating the license stanza and then appending the copyright text file located here:
${PROJECT_PATH_SOURCE}/licenses/deb-copyright
You should construct the license file as it is. Please keep in mind that this file is heavily governed by Debian Policy Manual and you should at least go through the specification for binary package described here: https://www.debian.org/doc/packaging-manuals/copyright-format/1.0/.
GENTLE REMINDER
Only need to generate the body of the file as the automation will generate the license stanza automatically. If there is a need to modify the process, consider overriding the output manually.

##### AutomataCI’s Long Description Generative Function
Due to the long description length ambiguity, AutomataCI relies on external data file for generating the DEB’s control file’s Description: long data field. The file is located at:
${PROJECT_PATH_RESOURCES}/docs/ABSTRACTS.txt
Please keep in mind that this data file is also shared by other packagers or release processes for maintaining consistencies.
The file MUST comply to:
1. Max column length of 69 characters per line; AND
2. Strictly text-only; AND
3. UTF-8 but do only use ASCII characters for maximum backward compatibility (means English only).
##### Testing Package
To test a built .deb package, simply use the following commands (when available):
$ dpkg-deb --contents “[NAME].deb”
$ dpkg-deb --info “[NAME].deb”